## Slide 1: Lesson 5 Python nightlight
Updated April 2026. Visit https://microbit.org/teach/ for most up-to-date resources.

## Slide 2: Recap: Python step counter

## Slide 3: Think: learning objectives
I can program a micro:bit using text-based code to make a light that switches on when it gets dark.
I can explain that sensors are inputs that sense things in the real world such as movement and light.
I can explain that logic is how computers make decisions in code based on whether things are true or false.

## Slide 4: Think: compare MakeCode to Python
Can you match instructions in MakeCode for a nightlight project with their equivalent in Python?
Notes: In Python there is no ‘then’ instruction, the colon : at the end of line 4 and the following indentation has the same effect.
Note how the indentations in the Python code are similar to the parts of the code in MakeCode that are snapped inside other blocks.
Python has an extra sleep instruction – like the pause block in MakeCode – because it makes the project work better by reducing the amount of flicker on the display when the light level is around 100. In MakeCode, the forever loops have built-in pauses that are hidden from users.

## Slide 5: Think: sensors
Sensors are inputs that sense things in the real world such as movement and light.
The micro:bit’s light sensor is built in to the LED display.
It measures light in a range from 0 (very dark) to 255 (very bright).
Notes: See the video on https://microbit.org/get-started/features/sensors/#light-sensor for more information on the light sensor.

## Slide 6: Think: logic
Logic is how computers make decisions in code based on whether things are true or false.
A conditional instruction (if… then… else) makes the decision to turn the LED lights on or off.
If the light level falls below 100, then it lights up the LEDs on the micro:bit’s display.
Else it clears the screen to turn the LED lights off.
Notes: Conditional (if…then…else) instructions are sometimes referred to as examples of selection.
In Python there is no ‘then’ instruction, the colon : at the end of line 4 and the following indentation has the same effect.
Python has an extra sleep instruction – like the pause block in MakeCode – because it makes the project work better by reducing the amount of flicker on the display when the light level is around 100. In MakeCode, the forever loops have built-in pauses that are hidden from users.

## Slide 7: Create: edit the code to make a nightlight
Edit or replace the existing code carefully so it matches the code here. Lower case and capital letters are important!
If you delete the existing code in the Python Editor, leave from microbit import * at the top.
Use auto-complete or the reference to help you.
Be careful to indent the code correctly.
Test your program in the micro:bit simulator which has a slider for light level.

## Slide 8: Create: send to micro:bit
Send the code to your micro:bit using the Send to micro:bit button at the bottom of the screen. Follow the instructions on screen.
Try the program out by covering the display and shining light on it. Does the program work as you expected?
Notes: Students transfer code to their micro:bits and test.
If you have battery packs, encourage students to unplug their micro:bits from computers and attach them.
Does it work as you expected? If not, do you need to edit the code and download it again?

## Slide 9: Create: tweak the program – light threshold
You may need to change the 100 number depending on the light levels around you.
Larger numbers will make the light come on more easily. Smaller numbers will make the light only come on when it’s darker.

## Slide 10: Create: tweak the program – moon and stars
Can you change the image to show a moon or star when it gets dark?
Note that LED brightness is represented as a number between 0 and 9, with 0 being off and 9 being the brightest.
Notes: You could use the LED planning sheet from lesson 3

## Slide 11: Create: tweak the program – flashing lights
You could attach the micro:bit to your bag or clothing to use as an additional safety light when walking or cycling.
Can you make the micro:bit flash to stand out more?
Think back to how you made the Python beating heart – can you do something similar with the code?

## Slide 12: Create: send to micro:bit again
Sending the code to your micro:bit again using the Send to micro:bit button at the bottom of the screen.
You might like to try the nightlight inside and outdoors to see how it works in different levels of light.
Notes: Students transfer code to their micro:bits and test.
If you have battery packs, encourage students to unplug their micro:bits from computers and attach them.
Does it work as you expected? If not, do you need to debug the code and download it again?

## Slide 13: Extend Use other sensors
Can you adjust your nightlight and turn it into an alarm that flashes if the temperature or sound levels are too high?
Note that the micro:bit measures temperature in degrees Celsius and measures sound in a 0-255 scale.
How might a temperature or sound alarm be useful in real life?
Notes: A temperature sensor could be used to help you decide if it is too hot to play sports or take a baby for a walk outside. A sound alarm could help you protect your hearing on a building site or when listening to music.

## Slide 14: Evaluate
How easy was it to code a nightlight in Python?
How did it compare with block-based coding?
Did the project work as you expected?
How did modify the code to show a moon and stars, or flashing lights, and why?

## Slide 15: Evaluate revisit the learning objectives
I can program a micro:bit using text-based code to make a light that switches on when it gets dark.
I can explain that sensors are inputs that sense things in the real world such as movement and light.
I can explain that logic is how computers make decisions in code based on whether things are true or false.
Notes: What is a sensor? An input that senses things in the real world, such as movement, temperature, and light levels.
What is logic? How computers make decisions based on whether things are true or false.
What is a conditional instruction? Sometimes also called selection, making different things happen based on different conditions.

## Slide 16: Next steps
Today we learned about the sensors and logic to make a nightlight.
Next time, we will learn about randomisation and selection to make a rock, paper, scissors game.

## Slide 17: Visit microbit.org/teach for more lessons, projects, courses and help.
This content is published by the Micro:bit Educational Foundation under a Creative Commons Attribution-ShareAlike 4.0 International (CC BY-SA 4.0) licence